## Slide 1: Codes on Random Geometric Graphs Dejan Vukobratović Associate Professor, DEET-UNS University of Novi Sad, Serbia Joint work with D. Bajović, D. Jakovetić, V. Crnojević (UNS)

## Slide 2: Codes on Random Geometric Graphs
Small Base Station
Sensor Node

## Slide 3: Codes on Random Geometric Graphs

## Slide 4: Codes on Random Geometric Graphs

## Slide 5: This talk will be about…
Inspiration: Codes on graphs
  LDPC codes and iterative decoding methods
Problem: Massive uncoordinated multiple access
  Evolution of Slotted ALOHA protocols
Motivation: M2M services in future 5G
  Connecting massive amount of devices to future 5G small cell network

## Slide 6: Outline
Single Base-Station Model
  Recent Trends in Slotted ALOHA
  LDPC Codes
Multiple Base-Station Model
  Cooperative Slotted ALOHA
  Codes on Random Geometric Graphs
Summary

## Slide 7: Outline
Single Base-Station Model
  Recent Trends in Slotted ALOHA
  LDPC Codes
Multiple Base-Station Model
  Cooperative Slotted ALOHA
  Codes on Random Geometric Graphs
Summary

## Slide 8: Slotted ALOHA
Preliminaries
system users
  Each user wants to send a packet over shared channel
  Time is divided in slots
  Users are synchronized to slots
Slotted ALOHA rules:
  Fully distributed, no coordination
  Every user applies the same rule:
    If a user has a packet to send, it will send it in upcoming slot
. . .
n users
. . .

## Slide 9: Slotted ALOHA
Users access slots with slot-access probability
Average slot load
    Idle slots are waste
    Singletons are useful
    Collisions are destructive
Throughput:
  Average fraction of singletons:
  (when )
. . .
. . .
n users
SA protocol
L. G. Roberts, “Aloha packet system with and without slots and capture,” SIGCOMM Computer Communications Review, Apr. 1975.

## Slide 10: Framed Slotted ALOHA
Frame
τ slots
Slots are organized in frames
If a user has a packet to send, it will send in upcoming frame in a randomly selected slot
    Average load is
Throughput:
  Average fraction of singletons:
  (when )
. . .
. . .
n users
H. Okada, Y. Igarashi, Y. Nakanishi, ”Analysis and application of framed ALOHA channel in satellite packet switching networks”, Electronics and Communications, 1977.
FSA protocol

## Slide 11: Collision Resolution Diversity Slotted ALOHA
CRD-SA protocol
Users repeat transmissions in multiple slots
  Repetition information in packet header
Same number of repetitions per user
    Collisions can be exploited
Iterative interference cancellation across slots
Throughput:
for CRDSA with two repetitions per user
E. Casini, R. De Gaudenzi, O. del Rio Herrero, “Contention Resolution Diversity Slotted ALOHA: An Enhanced Random Access Scheme for Satellite Access Packet Networks”, IEEE Trans Wireless Comms, April 2007.
. . .
. . .
n users
τ slots
Frame

## Slide 12: Collision Resolution Diversity Slotted ALOHA
Iterative Interference Cancellation (IIC)
Once the frame is finished, the base station performs IIC across time slots
    Iterative Interference Cancellation:
    Detect and decode clean signal (singleton)
  Remove its contribution from other slots
  Repeat while possible
E. Casini, R. De Gaudenzi, O. del Rio Herrero, “Contention Resolution Diversity Slotted ALOHA: An Enhanced Random Access Scheme for Satellite Access Packet Networks”, IEEE Trans Wireless Comms, April 2007.
. . .
. . .
n users
τ slots
Frame
. . .
. . .
    Recovery failure: Stopping Set!
    Complete recovery: Graph Erased

## Slide 13: Irregular Repetition Slotted ALOHA
IRSA protocol
Iterative interference cancellation equivalent to iterative erasure decoding of LDPC codes
Improved design (generalization of CRDSA)
  No. of repetitions varies across users
  Every user selects its no. of repeated transmissions (degree d) according to a predefined degree distribution
There exists an asymptotic threshold load G* below which probability user is collected
  G* ~ 0.97
. . .
. . .
n users
τ slots
user degree
slot degree
Frame
G. Liva, “Graph-Based Analysis and Optimization of Contention Resolution Diversity Slotted ALOHA,” IEEE Transactions on Communications, February 2011.

## Slide 14: Frameless ALOHA
Frameless ALOHA
Idea: Apply paradigm of rateless codes
No predefined frame length
  Slots are successively added until sufficiently many users are resolved
Optimization of the slot degree distribution
  Implicitly controlled through user behavior - slot access probability p
C. Stefanovic, P. Popovski, D. Vukobratovic, “Frameless ALOHA Protocol for Wireless Networks”, IEEE Communication Letters, December 2012.
. . .
. . .
n users
p
p
p
p
p
p
p
p
p
p
p
p
p
p
p
p
p
p
p
p
. . .

## Slide 15: SA vs LDPC
Modeled as LDPC codes for erasure channels
Goal: Max Throughput: T = G Pdec
Slotted ALOHA
Asymptotic analysis
  Density Evolution
Finite-Length analysis
  Stopping Sets
. . .
. . .
Decoding Probability Analysis
E.Paolini, C. Stefanovic, G. Liva, P. Popovski, “Coded Random Access: How Coding Theory Helps to Build Random Access Protocols”, IEEE Communications Magazine, to appear, arxiv.org/abs/1405.4127

## Slide 16: Outline
Single Base-Station Model
  Recent Trends in Slotted ALOHA
  LDPC Codes
Multiple Base-Station Model
  Cooperative Slotted ALOHA
  Codes on Random Geometric Graphs
Summary

## Slide 17: Multiple Base Station Model
Small Base Station
Sensor Node

## Slide 18: System model
Base station deployment, user locations
n users/devices, m base stations…
Base station
User/Device
…deployed independently uniformly at random over unit square area.

## Slide 19: System model
Transmission protocol
Run slotted ALOHA in parallel across all BS
  slots per frame – slot synchronized across all base stations
  User may be active (send packet replica) in several slots per frame
  User is heard by all base stations that cover it

## Slide 20: System model
System snapshot at slot t = 4
Signal at the base station j at slot t:
  sum of signals of all users active at slot t covered by the base station j
Base station
User active at t
User inactive at t

## Slide 21: System model
User collection
Base station “collects” a user whenever it detects a “clean” signal
A user is collected if it is collected by any base station!
User 2 decoded!
(t = 4)

## Slide 22: Asymptotic analysis
Asymptotic setup
and 0
where and
Probability of user collection:
  Upper bounded by user coverage probability
Normalized throughput:
Threshold Load:
Metrics of interest

## Slide 23: Decoding via Spatial Cooperation
Performed on a slot-by-slot basis

## Slide 24: Decoding via Spatial Cooperation
One iteration at arbitrary base station after each slot t
1) Check signal : BS j checks whether its received signal yj,t corresponds to a singleton; If yes, it performs Collect & Transmit step, otherwise it performs Receive & Update step
2) Collect & Transmit: BS j collects a user u and transmits xu to all BS k adjacent to user u (this is known to BS in advance). BS j leaves the algorithm.
3) Receive & Update: BS j scans all the received messages from its neighbors and identifies distinct set of user signals xu. Then it removes all the signals from this set from yj,t and goes to step one in the next iteration
Spatial Cooperation decoding algorithm
Fully Distributed: base stations communicate only with neighboring base stations!

## Slide 25: Main results
[Upper Bound on :
[Threshold Load]:
  The probability decreases at G = 0 from the value with negative slope equal at least
[Peak throughput scaling compared to single BS]:
  coverage
  Throughput ≥ x x throughput of single-BS frame slotted ALOHA
Spatial Cooperation:

## Slide 26: Decoding via Spatio-Temporal Cooperation
Each base station is doing:
1) Temporal decoding
2) Spatial decoding
Interchangeably…
Performed on a frame-by-frame basis

## Slide 27: Decoding via Spatio-Temporal Cooperation
One iteration at arbitrary base station after each frame of τ slots
1) Temporal SIC and Transmit: BS j performs Temporal SIC across its received slots within the frame. The set of recovered users is shared with neighboring BS’s and BS j goes to next step
2) Check Termination: If all the slots are recovered , BS j leaves the algorithm
3) Receive and Spatial IC: BS j scans all the received messages from its neighbors and identifies distinct set of yet unrecovered user signals xu. Then it removes all the signals from this set from all the slots where these users were active (activation slots are known for collected users) and goes to step one in the next iteration
Spatio-Temporal Cooperation decoding algorithm
Fully Distributed: base stations communicate only with neighboring base stations!

## Slide 28: Main results
[Lower Bound on :
[Threshold Load]:
  The probability stays at the maximum value at least in the range [0, ]
[Peak throughput scaling compared to single BS w iterative IC]
  coverage
  Throughput ≥ x x throughput of single-BS frame slotted ALOHA with iterative interference cancellation
Spatio-Temporal Cooperation:

## Slide 29: Optimal user degree distributions
Close to
single-BS optimal (IRSA)
Close to
constant-degree-two distribution
— average users’ spatial degree

## Slide 30: Simulation results

## Slide 31: Simulation results

## Slide 32: Summary
(Modern) coding theory helps designing efficient ALOHA-based random access protocols for single base station
For multiple base stations, geographic constrains need to considered, leading to codes on random geometric graphs
Work in progress, some results already available:
[Bajović, Jakovetić, Vukobratović & Crnojević, IEEE ICC 2014]
http://arxiv.org/abs/1401.6799
[Jakovetić, Bajović , Vukobratović & Crnojević, IEEE ISIT 2014]
http://arxiv.org/abs/1401.6810
[Jakovetić, Bajović, Vukobratović & Crnojević, IEEE Transactions on Communications, – to appear]
http://arxiv.org/abs/1407.1109